## Slide 1: Revisiting Carbon Accounting for Compost and Digestate
Megan Muller-Girard, Research Hub Manager
Notes: Excited to speak to you all about a project that’s been in the works for the last 8-9 months.
If you attended last year’s ORG conference, this may sound familiar. This is a follow-up from the presentation last year – explained the scope of project and what we planned to do.
Now can tell you a bit ab what’s been done!

## Slide 2: About the Research Hub
Sponsoring innovation, research, and development in the organics recycling sector
Annual project selection process
Call for Proposals
Proposal Survey
Evaluation Phase 1
Evaluation Phase 2
Jan-March
April/May
CCS & BCS feedback
July
Project(s) Selected
Proposals Shortlisted
May/June
Notes: Purpose of the Hub is to foster growth and innovation in the sector through R&D
In 2022, a proposal was submitted to develop a carbon accounting system for compost and digestate – thought this would be a really beneficial resource for the sector so it was chosen

## Slide 3: Project Background: Developing a methodology to calculate and report emissions for compost and digestate under the Greenhouse Gas Protocol
Objectives:
  To demonstrate to compost producers and AD operators the benefits of engaging with the GHG Protocol as a key step towards understanding their commercial activities within the global imperative to minimise climate-warming emissions.
  To provide guidance to operators on how to account for the production and application of compost and digestate under the GHG Protocol.
Worked with AECOM to deliver this project
Outcome: Carbon Accounting Methodology for Compost & Digestate
Notes: Objectives are -
Worked with AECOM – consulting firm - to develop a Carbon Accounting Methodology for Compost & Digestate based on standards and guidance published under the Greenhouse Gas protocol
I will give a little background into the foundations for this methodology and broadly what it includes
So to begin with our first objective – what are the benefits of engaging with the GHGP? Or in other words…

## Slide 4: Why should compost and digestate producers care about measuring and reporting carbon?
Climate crisis – Agriculture sector both a significant contributor of global emissions & heavily affected by climate crisis
Market forces – Increasing demand for GHG data from consumers and evidence-based Green Claims
Regulation – For larger organisations mandatory GHG reporting & climate-related disclosures
Notes: Climate – Agriculture sector both highly at risk from the impacts of climate change (flooding, extreme heat, etc.); also a major contributor
2020 - the ag sector contributed 11% to the UK’s total greenhouse gas (GHG) emissions (DEFRA, 2022).
Nitrogen synthetic fertiliser has been show to account for as much as an estimated 2% of global emissions (Menegat, Ledo, and Tirado, 2022).
So, by encouraging the use of less carbon intensive alternatives, compost producers and AD operators can support decarbonisation of ag sector
Market perspective –
consumers are also concerned ab the climate crisis and increasingly want to understand the environmental impact of their consumer choices.
And with more robust protections against greenwashing (e.g., EU Green Claims Directive), industries are increasingly expected to back up their green/eco claims with evidence.
Regulatory perspective –
For many large orgs it’s already compulsory under the Streamlined Energy and Carbon Reporting (SECR) regulations.
More transparent reporting of GHG emissions seems to be the direction of travel
Other reasons to measure your business’s greenhouse gas emissions? (from small-business-guide)
Save money – Helps identify which activities use a lot of energy and helps you reduce energy and resource use.
Generate business – if you reduce your costs you can become more competitive
Meet info demands of customers – helps you meet customer requests for info on GHG emissions – increasingly important part of procurement

## Slide 5: How can I begin to report my carbon emissions?
Notes: SO! Now that we’ve established WHY the industry should engage in carbon accounting and reporting, this leaves the question of HOW to actually do this. Which was the second objective of this project (click back to read)
Luckily for us, a lot of this work has already been done through the Greenhouse Gas Protocol (not reinventing the wheel) and the task for this project was to figure out how existing carbon accounting frameworks within the Greenhouse Gas Protocol could be applied to the production and use of compost and digestate

## Slide 6: The Greenhouse Gas Protocol (GHGP): Overview
Globally recognised standard focuses on developing a verifiable accounting and reporting emissions inventory.
Developed by World Resources Institute and World Business Council for Sustainable Development
Suite of standards and guidance documents that work together
  Standards provide a framework to measure & report GHG emissions
  Guidance provides clarity on how specific sectors can apply GHGP Standards
Notes: So, what is the GHGP? It’s an established and globally recognised initiative for accounting and reporting GHG emissions.
The way it works is the Protocol is comprised of a suite of standards and guidance documents that work together.
Standards set the reporting requirements
Guidance provides clarity on how business and governments can interpret and apply particular Standards.

## Slide 7: The Greenhouse Gas Protocol (GHGP): Relevant Standards & Guidance
Product Life Cycle Standard
Sets requirements for assessing the life cycle of a specific product
Corporate Standard
Original Standard - emissions sorted into Scopes 1-3
Used by organisations to prepare GHG emissions inventory
Land Sector and Removals (LSR) Guidance
Draft published Sept 2022, to be finalised mid-2024
Explains how emissions & removals are accounted within the land sector
Raw materials
Use
Disposal
Manufacturing
Transport to Customers
Notes: Product Life Cycle Standard:
Provides requirements for assessing the life cycle of a specific product, such as compost and/or digestate.
Main standard used for this project – reason: largely to allow producers to compare the emissions from their products to alternatives like mineral fertilisers
HOWEVER, if you’re not only interested in your product’s life cycle emissions but want to know the emissions from across your business, you would use the Corporate Standard
Corporate Standard:
Contains requirements and guidance for companies and organizations preparing a corporate-level GHG emissions inventory.
Categorises emissions into scopes 1-3
Both:
This project contains some guidance about aligning these two standards
Each of these Standards has associated guidance documents which were considered when compiling this methodology
The third piece of guidance the project looked into was the draft LSR guidance
Scope 1 covers emissions from sources that an organisation owns or controls directly – for example from burning fuel in our fleet of vehicles (if they’re not electrically-powered).
Scope 2 covers emissions that a company causes indirectly and come from where the energy it purchases and uses is produced. For example, the emissions caused when generating the electricity that we use in our buildings would fall into this category.
Scope 3 covers emissions that are not produced by the company itself and are not the result of activities from assets owned or controlled by them, but by those that it’s indirectly responsible for up and down its value chain. An example of this is when we buy, use and dispose of products from suppliers. Scope 3 emissions include all sources not within the scope 1 and 2 boundaries.

## Slide 8: The Greenhouse Gas Protocol (GHGP): Other considerations
Waste defined:
  GHG Protocol defines ‘waste’ as a co-product without economic value and, hence, has no allocated carbon emissions or removals
Land Sector – emissions and removals
  Land-based activities for compost & digestate
  Removals must be monitored indefinitely to provide evidence to the permanence of compost/digestate carbon storage in soils
Notes: In most cases, the compost and digestate life cycle starts with a waste (i.e. food/garden waste). But where purpose grown crops are used as inputs, this will impact your accounting.
Land-based activities for Compost and Digestate include
  Growing feedstock
  Application of final product to soil
  Whether these can be accounted depends if the feedstock waste
So, within the boundaries of the compost and digestate life cycle there are unlikely to be land-based emissions or sequestration from the atmospheric carbon pool to account for. The variation from this is where compost or digestate is produced from purpose-grown crops in which case the carbon sequestration is incorporated within the boundaries of the product lifecycle.

## Slide 9: Creating a Carbon Accounting Methodology for Compost/Digestate

## Slide 10: Carbon Accounting Methodology: Principles of Product Footprinting
Defining Scope and Boundaries
  Selecting a functional unit
  Identifying activities at each lifecycle stage that may contribute GHG emissions
Calculating Emissions
  Activity data * Emissions factor = GHG Emissions (tCO2e)
Report contains guidance on sourcing data, data quality indicators to consider, etc.
10
Notes: Defining Scope and Boundaries - First step of any GHG assessment – being very clear about what is being assessed
  Selecting a functional unit (e.g., kgCO2e per tonne of compost/digestate)
  Identifying activities that may generate GHG emissions and what data is required to calculate these emissions
  This has been done as part of the project – users just need to assess their activities and fit in their data accordingly
From there, the essential principle for calculating emissions comes down to this equation
  Activity data –ideally site/supplier specific data (e.g., distance travelled)
  Emissions factors – convert activity data into reportable GHG emissions (e.g., for x CO2 e are released per y distance travelled)

## Slide 11: Carbon Accounting Methodology: Putting Product Footprinting into Practice
Raw materials
Use
Disposal
Manufacturing
Transport to Customers
Product Life Cycle Standard
Compost & Digestate
Pre-Processing; Composting/AD
Packaging and Storage; Transport to end customer
Application to Land
Sourcing Feedstock (waste)
Packaging waste (disposal)
Calculate Emissions for each Lifecycle stage
  Key data requirements
  Worked example calculation
  Guidance on reporting
  A full worked example for compost and digestate
Notes: Figure 1 illustrates the activities at each stage of the life cycle which contribute to GHG emissions alongside the relevant standards and calculation methodologies from the GHG Protocol.
So the principle is to calculate the carbon associated with sourcing feedstock, then for any treatment steps and the actual composting/AD process itself, etc. etc. and then tally this all up for a total figure.
Report takes the reader through this to calculate emissions at each stage with data requirements and example calculations for each
Waste inputs - where the input feedstock is considered waste (i.e. food or garden waste) there are no direct emissions associated with the input feedstock, HOWEVER there are emissions associated with the transportation of the feedstocks to the production facilities. Also the embodied carbon and transportation of any additional materials should be considered within this stage, for example, packaging materials if required.

## Slide 12: Carbon Accounting Methodology: Corporate Standard Alignment
Raw materials
Use
Disposal
Manufacturing
Transport to Customers
Product Life Cycle Standard
Compost & Digestate
Pre-Processing; Composting/AD
Packaging and Storage; Transport to end customer
Application to Land
Sourcing Feedstock (waste)
Packaging waste (disposal)
Corporate Standard
Scope 3: goods & Purchased services
Scope 3: Upstream transport
Scope 1: Process emissions
Scopes 1 & 2: Energy
Scope 3: Use of sold products
Scope 3: End-of-life of sold products
Scope 3: Downstream transport
Scope 3: Waste
Scope 3: Water
Notes: So you can see these standards can work in alignment with one another – so while the project focused on product footprinting, it’s also possible to report organisational emissions under the corporate standard.

## Slide 13: Creating a Carbon Accounting Methodology: Report Contents
Overview of Greenhouse Gas Protocol
Carbon Accounting Methodology
  Instructions for calculating emissions for each lifecycle stage
  Guidance on reporting product footprint & corporate inventory
Supporting Information
  Annex A: Overview of GHG Accounting
  Annex B: Land Sector and Removals sample reporting template
  Annex C: Purpose-grown Crops – how to manage non-waste inputs
  Annex D: Literature review – used to define scope and boundaries of the assessment
  Annex E: Frequently asked questions
  Annex F: Example calculation - one tonne of purpose-grown crop liquor digestate
  Annex G: Spreadsheet containing additional worked examples & supporting info
Notes: WORKED EXAMPLES ARE A GUIDE to demonstrate how to utilise the methodology and provide a theoretical value. Not a one-fits-all.
Final values will depend on each composters/ad operators’ unique process. Very important to tailor your calculations accordingly

## Slide 14: Key Takeaways
Reasons to count your carbon!
  Climate crisis - potential to decarbonise
  Market forces - consumer choices
  Regulation - mandatory reporting
Project Outcome - comprehensive methodology to apply Product Standard to composting & AD processes (with Corporate Standard alignment)
Per the GHGP, ‘waste’ has no allocated carbon emissions or removals
Draft LSR Guidance* specifies that removals must be monitored indefinitely to prove the permanence of compost/digestate carbon storage in soils
May be used to demonstrate your product footprint against mineral fertilisers
*This guidance is in currently in draft form. Details may be subject to change in the final published document.
For a full picture, we encourage you to read the completed report!

## Slide 15: Thank You!
To Access the Report, contact
Megan Muller-Girard
  Research Hub Manager
  megan@realschemes.org.uk
Free to CCS & BCS Participants
Special thanks to Jenny Grant and Jesse Scharf for their contributions to this work through the Project Management Team!
Acknowledgements